## Slide 1: 室內定位演算法
2024 嵌入式系統設計 期末專題報告
312513028 盧昱愷
311513126 陳亮宇

## Slide 2
利用iBeacon達成室內使用者位置即時定位
觀察場地配置，可能不利於Propagation Model-based
決定利用Fingerprinting-based演算法
動機&目標

## Slide 3
選擇區域 (Improved KNN[1])
  找出和目前RSSI最接近的K個參考點。
  創建K類，各類中心分別為所選K個參考點。
  若其他參考點和該類中心 < M公尺， 則加入該點成為該類成員。
  選擇成員最多的類。
避免過於遙遠的參考點影響結果
演算法說明-1

## Slide 4
Selected Reference Points
Real Position
Predicted Position
1. 理想情形
2. 實際情形
3. 區域選擇

## Slide 5
利用所選的類計算加權座標(M-WKNN matching algorithm[2])
考慮RSSI與實際距離的關係為非線性
演算法說明-2

## Slide 6
利用所選的類計算加權座標
演算法說明-2
Notes: 所選參考點
𝑃_𝑖所選參考點

## Slide 7
App簡介
目前接收資料 最新10筆平均
定位開關 判定座標結果
RSSI折線圖
切換區域
目前接收數量

## Slide 8
實驗數據
Area
  X軸距1.2m
  Y軸距0.6m
  約80個參考點，各參考點一筆RSSI
Coordinate
  X軸距0.7m
  Y軸距0.6m
  約110個參考點，各參考點一筆RSSI

## Slide 9
誤差來源
  打點時位置量測錯誤
  人體干擾
  iPad面向方向
精準度僅達公尺級
改進方向
  提升參考點密度及數量
  適應性更改分類數量(K)及判斷距離(M)
實驗結果

## Slide 10: 參考資料
[1] S. A. Zibaei and R. Ali Abbaspour, "Evaluation of Improved K-Nearest Neighbors for Indoor Positioning System in Real Complex Buildings," 2023 9th International Conference on Web Research (ICWR), Tehran, Iran, Islamic Republic of, 2023, pp. 12-19, doi: 10.1109/ICWR57742.2023.10139137.
[2] W. Liu, X. Fu, Z. Deng, L. Xu and J. Jiao, "Smallest enclosing circle-based fingerprint clustering and modified-WKNN matching algorithm for indoor positioning," 2016 International Conference on Indoor Positioning and Indoor Navigation (IPIN), Alcala de Henares, Spain, 2016, pp. 1-6, doi: 10.1109/IPIN.2016.7743694.